## Slide 1: Getting Started with Raspberry Pi (RPi)
By: Yeo Kheng Meng (yeokm1@gmail.com)
https://github.com/yeokm1/getting-started-with-rpi
Creative Crew (12 Aug 2016)

## Slide 2: About me
Hardware Engineer at Algo Access
My Hardware projects with Arduino and Raspberry Pi

## Slide 3: Who is this talk for?
Beginners to the world of hardware/Internet-of-things
People transitioning from Arduino to RPi

## Slide 4: What is a Raspberry Pi (RPi)?
The Raspberry Pi is a series of credit card-sized single-board computers developed in the United Kingdom by the Raspberry Pi Foundationto promote the teaching of basic computer science in schools and developing countries
https://en.wikipedia.org/wiki/Raspberry_Pi

## Slide 5: Types of Raspberry Pi
Model B+ (2014)
2 Model B (2015)
Model A+ (2014)
700Mhz single-core ARMv6
256MB Ram
1 USB port
No Ethernet port
700Mhz single-core ARMv6
512MB RAM
4 USB ports
Ethernet port
900Mhz quad-core ARMv7
1024MB Ram
4 USB ports
Ethernet port
3 Model B (2016)
1.2Ghz quad-core ARMv8
1024MB RAM
4 USB ports
Ethernet port, Wifi, Bluetooth
Zero (2015)
1Ghz single-core ARMv6
512MB RAM
1 USB OTG port
Micro-HDMI
Compute Module (2014)
700Mhz single-core ARMv6
512MB RAM
4GB onboard flash
SODIMM connector
Model B (2012)
700Mhz single-core ARMv6
256MB RAM
2 USB ports
Ethernet port
Obsolete (Do not purchase unless you have special reasons)
Special Mention

## Slide 6: Arduino vs Raspberry Pi
Specs | Arduino Uno | Raspberry Pi 3 Model B
CPU type | Microcontroller | Microprocessor
Operating System | None | Linux (usually Raspbian) or Win 10
Speed | 16 Mhz | 1.2Ghz
RAM | 2KB | 1GB
GPU/Display | None | VideoCore IV GPU
Disk | 32KB | Depends on SD card
GPIO pins | 14 digital pins (includes 6 analog) | 26 digital pins
Other connectivity | None | USB, Ethernet, HDMI, audio
Power consumption | 0.25W | 6W

## Slide 7: Minimum to get started
Raspberry Pi 3
HDMI monitor
USB Keyboard
USB Mouse
2.5 Amp USB Power Adapter
Micro-USB cable
8GB Micro-SD card
Computer to load initial card image

## Slide 8: Step 1: Download SD card image
Download *.img files from
  https://www.raspberrypi.org/downloads/
  https://www.raspberrypi.org/downloads/raspbian/
Beginners should pick Raspbian Jessie

## Slide 9: Step 2: Write image to SD card
Windows computer
  https://sourceforge.net/projects/win32diskimager/
Mac and Linux computer
  Get drive number of SD card
    sudo fdisk –l
  Write disk image to drive number N
    sudo dd if=path_of_your_image.img of=/dev/rdiskN bs=1m

## Slide 10: Step 3: Boot Raspberry Pi from SD card
Might take a few minutes for the first time

## Slide 11: Step 4: Initial Configuration
Set locale to Singapore
Set keyboard layout to English (US)
Configure locale and time zone

## Slide 12: Step 5: Do a system update
Connect to the Internet
Open the terminal
Look for new system updates
  sudo apt-get update
Download and install latest updates
  sudo apt-get upgrade
Recommend to reboot after that

## Slide 13: Available Applications
Web Browser:
Office Applications: Libreoffice
Media Player: VLC

## Slide 14: Raspbian default username/password
Username: pi
Password: raspberry

## Slide 15: File System Directory layout
/home/pi or “~”
  Your “Home” directory
Removable Drives at
  /media/pi/….

## Slide 16: Header pins
26 Digital-only General Purpose Input Output pins
3.3V logic levels
  Arduino uses 5V

## Slide 17: Using the GPIO pins
Python programming language
LED
Button

## Slide 18: LED and Button Connection
Parts
Breadboard
Button
1x 10K ohm pull-down resistor
Button
1x 220 ohm resistor

## Slide 19: LED Blinky
Blink LED at 1 second intervals using Python
python led.py

## Slide 20: LED and button code 1
Button press supposed to toggle LED status
python button1.py

## Slide 21: LED and button code 2 (Debouncing)
Button press now toggles LED correctly
python button2.py
  Observe CPU usage: “ps aux | grep python” or Task Manager

## Slide 22: LED and button code 3
Toggle LED without sucking CPU resources by sleeping a little in the loop
python button3.py
  Observe CPU usage: “ps aux | grep python” or Task Manager

## Slide 23: My internet radio streamer project
https://github.com/yeokm1/pi-radio

## Slide 24: Some warnings
RPi does not keep time on poweroff
  No onboard battery and Real-Time-Clock (RTC) chip
  It can sync time when connected to network
Do not connect current-heavy USB devices
  600mA for all USB ports default. Can increase to 1.2A
  In: /boot/config.txt Add: max_usb_current=1
  2.5A resettable polyfuse
  Use powered USB-hub if needed

## Slide 25: Q&A